COMMUNICATION HP-71 <=> PC

		      Michael Markov (PPC Paris 301)


This file documments three HP-71 programs I use to upload and download files to
and from my HP110. They can also be used to do the same with IBM PC or
compatible machines equipped with an HP82973 HPIL Interface.

Why do I need special programs to do this, when HPILLINK provides the ability
to upload and download files from the PC keyboard? Because I only want to
exchange files with the PC, not use a remote keyboard for my HP-71. The editor
I have on the PC or the HP110 (Ed Gilbert's Editor, NOT memomaker) is much
faster than any text editors I have on the HP-71, they handle long text files
without slowing down to the speed of cold molasses, and have features HP-71
users only dream of. Editing BASIC programs is usually faster without the delays
introduced by the remote keyboard. Finally - HPILLINK set-up with the remote
keyboard does a number of unfriendly things, such as mess-up my STARTUP, my key
assignments, or even FREEPORT memory I do not want FREEPORTED, if I do not have
KEYBOARD LEX in my machine.

Still, it is nice to have mass storage and printers at work, by way of HPILLINK
and the IBM XT in my department. Being able to share data stored in my HP-71
using the HPILLINK /C option helps keep my bosses happy with my HP-71. Hence,
the routines below.

NOTE: LINK 1.02 (Southern Software) provides similar capabilities. I hear there
soon will be a new version called LINK PLUS, with many interesting features.
I use LINK 1.02 rather than HPILLINK if I want to use the PC as a printer or
as a video interface for my HP-71. 
   
The first program is intended to upload or download a single file at a time,
from the HP-71 keyboard. Before using this program, you must run the
HPILLINK.EXE program on the PC, and connect the HP-71 to the PC HP-IL port.

When you download a file, you must provide the full file name, such as:
JUNK.TEX

When you upload a file, the program will automatically supply the correct file
extension if you have the FTYPE$ keyword available. See source code below.
If not, the extension will be left blank, and you will have to RENAME the file
from the PC keyboard if you want the correct extension.

The file transfer takes little or no time. Once done, disconnect the HP-71,
exit HPILLINK with the F8 key, and do whatever you desire with either the PC or
the HP-71. Enjoy! 


0010 ! PC71EX - Transfer HP71 files between a PC and an HP71 with HPILLINK
0020 ! Copyright Michael Markov 1988
0030 ! 
0040 ! Uses FTYPE$ keyword from DATACOM ROM - See FLTYPELXS for source
0050 ! This is required if you want to provide the proper file extension
0060 ! when uploading files to an IBM PC via HPILLINK /HP82973 Interface card
0070 ! or to an HP110 running HPILLINK.
0080 ! 
0090 ! If you do not have the FTYPE$ keyword, comment-out the line 300 :
0100 ! 300 T$=FTYPE$(F$)
0110 ! 
0120 ! The advantage of this program is that it allows file transfers without
0130 ! messing-up your favorite STARTUP, your key assignments, or FREEPORTing
0140 ! stuff you may not want free-ported. This was developed when I started
0150 ! to make heavy use of my HP110 to edit HP71 source code files, which I
0160 ! then assembled using the AREUH (PPC-Paris) assembler-linker before 
0170 ! downloading the resulting LEX for testing in the HP71. I had no need for
0180 ! an external keyboard since the EDITOR I use on my HP110 is considerably
0190 ! faster than EDTEXT, and provides more flexibility.
0200 ! 
0210 LOCAL @ DISP 'Up or Download?(U/D)'
0220 A$=UPRC$(KEYWAIT$) @ IF A$='D' THEN 240
0230 IF A$='U' THEN 280 ELSE 210
0240 LOCAL @ INPUT 'DOWNLOAD FILE? ';F$ @ IF F$='' THEN END 
0250 P=DEVADDR(':PC')
0260 SEND UNT TALK P DDT 0 UNT MTA LISTEN P DATA F$ EOL 
0270 COPY :P @ GOTO 240
0280 INPUT 'Upload file? ';F$ @ IF F$='' THEN END 
0290 P=DEVADDR(':PC') @ T$=''
0300 T$=FTYPE$(F$)[1,3] ! comment out if FTYPES keyword not available
0310 SEND UNL LISTEN P MTA DDL 0 DATA F$,'.',T$,10 
0320 COPY F$ TO :P @ GOTO 280

The second program is a minor variant of the PC71EX program given above. It
allows you to upload or download ROM images just as if the PC was an HPIL disk
drive. There is one interesting difference: the file stored on the DOS disk will
take less space than on HPIL mass storage. Apparently, HPILLINK and ROMCOPY
version RCPY:E were designed to work together better than the mass storage
option! Here, we see the advantages of an intelligent mass storage device.

0010 ! PCROM - Transfer HP71 ROM images between a PC and an HP71 with HPILLINK
0011 ! and ROMCOPY LEX.
0020 ! Copyright Michael Markov 1988
0030 ! 
0040 ! This program is a slightly modified version of PC71EX, elsewhere on this
0041 ! swapdisk. See PCCOMM for documentation.
0042 ! 
0210 LOCAL @ DISP 'Up or Download?(U/D)'
0220 A$=UPRC$(KEYWAIT$) @ IF A$='D' THEN 240
0230 IF A$='U' THEN 280 ELSE 210
0240 LOCAL @ INPUT 'DOWNLOAD FILE? ';F$ @ IF F$='' THEN END 
0241 INPUT 'To :PORT(#)? ','5';N
0250 P=DEVADDR(':PC') @ IF NOT POS(F$,'.ROM') THEN F$=F$&'.ROM'
0260 SEND UNT TALK P DDT 0 UNT MTA LISTEN P DATA F$ EOL 
0261 X=POS(UPRC$(F$),'.ROM') @ F$=F$[1,X-1]&':'&STR$(P)
0270 ROMCOPY F$ TO ':PORT('&STR$(N)&')' @ GOTO 240
0280 INPUT 'Upload file? ';F$ @ IF F$='' THEN END 
0281 INPUT 'From :PORT(#)? ','5';N
0290 P=DEVADDR(':PC') @ X=POS(UPRC$(F$),'.ROM') @ IF X THEN F$=F$[1,X-1]
0310 SEND UNL LISTEN P MTA DDL 0 DATA F$,'.ROM',10 
0320 ROMCOPY ':PORT('&STR$(N)&')' TO :P @ GOTO 280

The last program allows you to upload many files to the PC, under the control
of an HP-71 program. I have used it to transfer entire swapdisks to my HP110,
for friends that have HP-71 machines and PC's, but not HP9114 drives. They then
read the disks as best they can. I understand that there is a new package from
Personalized Software called READHP, that allows IBM machines to read 3.5" disks
formatted by HP machines.

It should be possible to download files from the PC with a PCTODISK program,
just as easily as you can upload entire disks. The easiest approach would be
to start things going by creating a TEXT file with all the desired filenames
and extensions with the DIR A: >DIR.TEX. Then use PC71EX to download the file,
and let your HP-71 control the download to an HPIL mass storage device. I have
not needed to do this, since I am not (as of this date) getting any
contributions on DOS disks. However, if HP abandons HPIL, this may be the only
way to have peripherals for our HP41/HP75/HP71 computers, may they last many
years. (Have you purchased a spare HP-71 yet? NO? Why?).

NOTE: PCTODISK does not yet exist, except as an idea. It is one of my many
'to do sometime' projects.

Anyways, easy PC<==>HP71 communications will greatly ease the transition to the
world of DOS/OS2 machines, where instead of HP BASIC you will be forced to learn
PASCAL, C, MEGA BASIC or QUICK BASIC if you want to do any serious programming.
   
Obvioulsy, the PC must be running HPILLINK, and the default drive to which 
HPILLINK writes the files should be as empty as possible. Load HPILLINK with
A:HPILLINK, then replace the disk in the default drive (usually A:) with a
newly formated disk. On the HP71, run DISKTOPC. When the program stops, replace
the disk in the default drive, and run DISKTOPC on the HP71 to continue the
upload.

NOTE: Do NOT purge the temporary directory file (default DIRFL), except at the
start of the upload, before the first file is transfered. This allows the PDIR
keyword (JPCROM) to create a new file that contains all the information you need
to upload the disk. The HP-71 automatically deletes file entries as the upload
goes on. Any time the DISKTOPC program stops, you can LIST DIRFL to find out
how many files still ave to be uploaded.

Note that the program polls the PC to determine whether the remote load failed
for any reason, such as no space remaining available on the PC. This program is
intended to be used in conjunction with a video interface on the HPIL loop.

The program uses JPCROM to create a directory listing of the disk to be
uploaded to the PC. This is by far the most convenient way. Among other things,
JPCROM implements a poll handler that allows your HP-71 to identify HP-41,
HP-75 and other non-HP71-standard file types. This allows you to tag the file
names to help identify the contents of the file. HPILLINK does not recognize
HP-41 or HP-75 file types. In fact, it does not recognize all HP-71 file types,
atleast, not the version I have (Maybe revision E does better, but I do not have
that yet. 

It should be obvious that minor changes to line 240 allow uploading only HP-71
files, or only HP41 files, etc, should you so desire.

0010 ! DISKTOPC - UPLOAD FILES TO PC WITH HPILLINK
0020 ! This program is available, at least in concept, in the HPILLINK
0030 ! documentation. It implements the task in a way that helps minimizes
0040 ! user intervention. It was written to facilitate uploading Swapdisks
0050 ! to an IBM PC equipped with an HPIL interface card.
0060 ! 
0070 ! Since the HP71 is the controller, you can have a disk drive on the loop,
0080 ! and copy each file from the drive to the IBM PC, using a minimum of
0090 ! HP-71 memory.
0100 ! JPCROM REQUIRED. IF NOT AVAILABLE, CREATE DISK DIRECTORY LISTING WITH
0110 ! SOME BASIC ROUTINE SUCH AS DIR71
0120 CONTROL ON @ RESET HPIL @ RESTORE IO @ DISPLAY IS :DISPLAY
0130 INPUT "Which drive? ";D
0140 P=DEVADDR('%16('&STR$(D)&')')
0150 INPUT 'temp. file? ','DIRFL';F$
0155 ON ERROR GOTO 161
0160 PDIR :P TO F$ @ GOTO 169
0161 OFF ERROR @ DISP ERRM$;'Purge? (Y/N)'
0162 A$=UPRC$(KEYWAIT$) @ IF A$='Y' THEN PURGE F$ @ GOTO 155
0169 OFF ERROR @ ASSIGN #1 TO F$ @ RESTORE #1
0180 DIM A$[60] @ D=DEVADDR(':PC') @ STANDBY ON @ REMOTE 
0190 FOR I=0 TO FILESZR(F$)-1 @ READ #1;A$ @ DISP I;A$
0200 IF SPOLL(D)#5 THEN 270
0210 F$=TRIM$(A$[1,10])
0220 T$=TRIM$(A$[14,19])[1,3]
0230 IF T$='41:' OR T$='75:' THEN G$=F$&T$[1,2] @ T$='UNK' ELSE G$=F$
0240 SEND UNL LISTEN D MTA DDL 0 DATA G$,'.',T$,10 
0250 COPY F$&':'&STR$(P) TO :D
0260 NEXT I
0270 LOCAL @ DISP 'HP110 Drive A full-delete last file copied'
0280 READ #1,I-2;A$ @ DISP 'last file copied: ';I-2;A$
0281 FOR J=I-2 TO 0 STEP -1 @ DELETE #1,J @ NEXT J
0290 STANDBY OFF @ CONTROL OFF @ END 

       LEX    'FTYPELEX'  LEX file name
       TITLE  FTYPELEX, File type LEX,  Samuel H Chau [242]
*
       ID     #F6         compatible with DCLEX in DATACOMM ROM
       MSG    0           no message table
       POLL   0           no poll handler
*
       ENTRY  FTYPE
       CHAR   #F          string function
*
       KEY    'FTYPE$'    Syntax: FTYPE$('file specifier') or
*                                 FTYPE$(assign channel #)
*                         Returns file type as a 5-char string
*                         Null string returned if file not found
*                         Example:  FTYPE$('FORTHRAM') returns FORTH
       TOKEN  1
       ENDTXT             end of text table
************************
*      **** EQUate Table ****
*
AVE=D1 EQU #18BB8 update AVMEME from D1 or C
BSERR  EQU #0939A BASIC system error
D0=AVS EQU #09B2C set D0 to address in AVMEMS
D1MSTK EQU #1954E set D1 at MTMSTK (AVMEME)
FDCH#  EQU #114AC find channel # in assign table
FFIB#  EQU #122EF find file number in FIB
FILXQ$ EQU #09B95 filename execute for a string expression
FINDF  EQU #09F77 find a file
FLTDH  EQU #1B223 convert 12-digit flt to HEX integer
FNRTN  EQU #0F23C function return
FTYPDC EQU #06902 file type decompile
FUNCR0 EQU #2F89B function scratch RAM start
POLL   EQU #12337 poll LEX files with process #
POPMTH EQU #1B3DB skip past item on MATH stack
RSTK<R EQU #014A8 restore RSTK level(s) from RSTKBF buffer
R<RSTK EQU #014DD save RSTK level(s) into RSTKBF buffer
STRHED EQU #14C2E generate string head on stack
pFINDF EQU #00017 poll to find a file
pFSPCx EQU #00005 poll to execute file specifier
eFSPEC EQU #0003A invalid filespec error
*
************************
*
       NIBHEX C11    one string or numeric parameter
FTYPE  CD0EX
       RSTK=C        save D0 (PC) on return stack
       GOSBVL R<RSTK save RSTK level(s)  [P=0]
       A=DAT1 W      get top of MATH stack in A
       LCHEX  A      load C:0 for parameter type check
       ?C>A   P      integer parameter?
       GOYES  FTYP03 yes: interpret as channel #
       A=A+1  P
       ?A#0   B      not string parameter?
       GOYES  FTYP01 yes: parameter is invalid
       GOTO   FTYP09 no: interpret string as file specifier
FTYP01 LC(4)  eFSPEC load Invalid filespec error
FTYP02 GOVLNG BSERR  BASIC error exit
FTYP03 D1=D1+ 16     pop integer argument off MATH stack
       GOSUB  ave=d1 update stack top pointer
       GOSBVL FLTDH  convert 12 form channel # to HEX integer
       B=A    B      put HEX form in B for FDCH#
       GOSBVL FDCH#  find channel # in assign table
       GONC   FTYP08 not found: ready for exit
       ?A=0   B      channel closed? no: A(B)=FIB#
       GOYES  FTYP08 yes: punt!
       GOSBVL FFIB#  find file # in FIB
       GOC    FTYP08 not found? yes: punt! no: D1 @ file # in FIB
       D1=D1+ 5      advance to file type entry in FIB
FTYP04 GOSBVL D0=AVS set D0 to AVMEMS
       C=0    W      preclear C
       DAT0=C W      blank out word at AVMEMS
       D0=D0+ 2      point past one null
       GOSBVL FTYPDC get file type (5 chars), D0 points past it
       GOSUB  d1mstk set D1 to AVMEME
       GOSBVL D0=AVS set D0 to AVMEMS
       C=DAT0 W      get file type in C
       ?C=0   B      not at file type string?
       GOYES  FTYP06 yes: move pointer down
FTYP05 ?C=0   B      end of file type string?
       GOYES  FTYP07 yes: ready for string return
       D1=D1- 2      point D1 down 1 char
       DAT1=C B      push one ASCII char onto stack
FTYP06 CSR    W
       CSR    W      shift to next char in file type string
       GOTO   FTYP05 continue building string on stack
FTYP07 GOSBVL STRHED generate string header on stack
       GOSBVL RSTK<R restore RSTK level(s)
       C=RSTK
       CD0EX         restore D0 (PC) from RSTK
       GOVLNG FNRTN  function return
FTYP08 GOSUB  d1mstk set D1 to AVMEME
       GOTO   FTYP07 return with string
FTYP09 GOSUB  ave=d1 update stack top pointer
       C=DAT1 W      read string header into C
       CSR    W
       CSR    W      shift to string length field
       ?C=0   A      null string?
       GOYES  FTYP08 yes: ready for return
       GOSBVL FILXQ$ execute tokenized file specifier
       P=     0
       LCASC  '  '   load C with 2 ASCII spaces
       R0=C          save in R0
       GOC    FTYP16 file specifier is mainframe recognizable
       GOSBVL POLL   illegal: issue file spec execution poll
       CON(2) pFSPCx file specifier execute poll
       GOC    FTYP13 error return from poll: error exit
       ?XM=0         pFSPCx poll handled? 
       GOYES  FTYP10 yes: continue
       GOTO   FTYP01 no: Invalid filespec error
FTYP10 C=R0          last 2 chars of filename into C
       R1=C          save in R1
       R0=A          filename (blank filled) into R0
       GOSUB  d1mstk set D1 to stack top
       GOSBVL POPMTH skip past current item on stack
       GOSUB  ave=d1 update stack top pointer
       GOSBVL POLL   issue poll to find file
       CON(2) pFINDF file finder poll
       GONC   FTYP11 no error: continue
       A=C    A      save C in A
       LCHEX  16     load C with HPIL File not found error #
       ?A=C   B      file not found on HPIL mass storage?
       GOYES  FTYP12 yes: ready for return
       C=A    A      restore C from A
       GONC   FTYP13 B.E.T.
FTYP11 ?XM=0         pFINDF poll handled?
       GOYES  FTYP14 yes: continue
FTYP12 GOTO   FTYP08 no: ready for return
FTYP13 GOTO   FTYP02 load BASIC error returned from LEX file
FTYP14 D1=(5) FUNCR0 set D1 to function scratch RAM
       C=R0
       DAT1=C W      put file attributes into function scratch RAM
       D1=D1+ 11     advance to file type field
FTYP15 GOTO   FTYP04 go find file type
FTYP16 GOSUB  ave=d1 update stack top pointer
       GOSBVL FINDF  find the file
       GOC    FTYP12 not found: ready for return
       D1=D1+ 16     move to file type field in file header
       GONC   FTYP15 B.E.T.
ave=d1 GOVLNG AVE=D1
d1mstk GOVLNG D1MSTK
       END