PICTURE  DESCRIPTIONS

mb1.jpg
Steve Goldstein and Mark Barton posing at the base of the still-to-be-wound coil form.  The form is mounted to the primary base and has most of the upper terminal assembly mounted on it.  This was shot after a gantry raising test.  We wanted to make sure the hydraulic gantry mechanism worked OK before we invested in coil winding.  The form itself is a 4 x 11 foot fiberglass tank purchased from Ryan Herco plastics.  When fully assembled with the upper ball (missing in photo), it stands a full two stories.

mb2.jpg
Me (MB) holding the switch to the hydraulics during the above mentioned test.  The coil is on its way up or down; I can t tell from the picture.

mb3.jpg
Secondary being wound.  The two guys in the foreground are mixing and applying liquid silicone to the winding as it is going on.  The wire is 14awg untinned stranded with 40KV silicone insulation.  It was specially manufactured by Dearborn Wire and Cable because their standard product came tinned and I was more interested in the electrons zooming through copper instead.  There is almost exactly one mile of wire on the secondary which resonates at 50KHz with the upper terminal.

mb4.jpg
Closeup of upper terminal assembly.  This consists of 9 spun aluminum spheres each 20 inches in diameter.  There are 7 spheres arrayed in a circle around a central sphere connected by aluminum pipes.  The whole thing represents a piecewise approximation of a toroid (expensive, but not nearly as expensive as a huge toroid, and easier to handle).  The star pattern precludes any possibility of the upper terminal looking like a shorted turn (although I have never seen any evidence of this effect).  The central sphere is mounted to a birthday-cake-sized insulator we made out of pure epoxy resin which has a pipe fitting cast into it.  The ninth sphere (not shown) mounts to the vertical pipe.  (Little water heater not part of project.)  

mb5.jpg  and  mb6.jpg
Full outside view of trailer, coil slightly raised, upper terminal being assembled.  The trailer is 8 feet wide and 18 feet long with 4 foot walls and houses the coil as well as all other components ( Have Coil Will Travel ).  After the upper terminal is assembled, the coil is fully raised to vertical, the hinge pins are removed and the trailer is driven away.  mb6 shows a good view of the completed upper terminal with discharge rods.  A specially fitted  boat  cover shelters all when not in use.

mb7.jpg
Closeup of 4 foot cube primary base.  The primary is made from 1" copper tubing and the box below it contains the interrupter.  This shot was taken during the coefficient of coupling measurements I have talked about in previous posts.  For a complete description of the measurement technique used, see my article titled  Using your Stereo to Measure Coupling  in TCBA News, Vol 13, #2, Apr-May-June 1994.  The technique is a modern day equivalent of the procedure used by Tesla in Colorado.

mb8.jpg
Trailer interior.  At the right of the picture, which is actually the head of the trailer, stands the 18KV, 45KVA dry-type transformer with its cover removed.  This was built for us by Matra Electric, Inc. and weighs a mere 800 pounds.  Our contact at Matra confided that the transformer can be pushed to almost double its rating for brief periods!  We wanted a dry-type transformer because it is illegal to operate oil filled units indoors and we wanted to be able to drive the trailer onto sound stages and the like.  To its immediate left can be seen the diode assemblies we built for our DC power experiments.  The next cabinet to the left contains the output charging choke, filter capacitor bleeder resistors (hanging from top) and the 70KV Jennings  don't-die  relay.  This normally-closed HV vacuum relay opens and closes with the power to the interrupter, so when the interrupter is shut off, it quickly discharges the 7uF filter capacitor through a 5K HV resistor.  This relay is aptly named and is a double safety with the bleeders.  Still, we are always VERY AFRAID and exercise EXTREME CAUTION.  Also, not seen in the picture are another HV diode in series with the output choke, and the 100Mohm resistor used for metering.

mb9.jpg
Outside view of DC power supply cabinets with the doors closed.  The blue gallows above the first cabinet is part of the pulley mechanism which raises and lowers a core made of silicon steel laminations in and out of the output choke.  This controls the charging time constant.  The pulley cable goes to an electric winch which is operated from the main panel.  To the left are the power supply filter capacitors.  These are two Maxwell Labs 14uF @ 20KV caps wired in series for 7uF @ 40KV.  All HV wiring is done with the 40KV silicone wire snaked inside thick wall vinyl tubing which seems to be standard industry practice by places like Hughes Aircraft.

mb10.jpg
Closeup of rectifier and power supply choke assembly.  Each PVC tube contains 25 6A10 diodes in series.  These diodes are 6 amp @ 1000V PIV each and fairly inexpensive.  There is a 1Mohm resistor and a .001uF/1500V ceramic disk capacitor across each diode for equalization of AC transients and voltage distribution.  Two tubes in series form one rectifier leg.  There are 8 tubes in all wired as a full wave bridge.  The two white chokes on either side are wound on 3 inch PVC and have laminated cores.  These follow the diodes to form a balanced choke input filter.  The chokes are wound with 22awg hookup wire in sections separated by plexiglass plates and can withstand very high voltages.

mb11.jpg
Trailer interior, right wall, main control panel.  The four meters read AC line voltage, AC line current, DC voltage on filter caps, interrupter firing rate.  For the latter, it was an easy matter to design a circuit that looked at the DC cap ripple and convert it to a voltage to drive the meter with a F/V converter.  The small black meter is a low voltage vernier for the HVDC allowing one to watch the caps discharge all the way to zero.  This meter may be read when the little button below it is depressed.  The two knobs control interrupter motor speed and something that for the life of me I just can t remember.  It has been five years since I have touched this project and unfortunately we didn t get around to labeling the panel.  Doh!

mb12.jpg
Night of the first test.  This photo shows the coil doing 16.5 feet on its first run.  We were eventually able to squeeze another 9-10 feet out of it, but we still fell far short of our design coil of 35-40 feet.  I now know what we did wrong (primary cap too large!) and my thanks to all on the Tesla groups for sharing your insights.  The trailer has been moved to a new location after resting dormant for five years and we shall procede again toward our goal.  The discharge rod between the upper ball and the spark is not visible in this night shot.