PICH1024.GIF and PICH800.GIF

 These are scans (1024x768 & 800x600) taken from a B&W photo of a
 Tesla coil designed by Jeff Mullins, and built by master coiler
 Gary Legel. The entire coil stands five feet from the floor, in-
 cluding the 12 x 3 toriod mounted on top of the secondary. The
 secondary coil is wound on a three inch diameter by twelve inch
 long polystyrene tube and has 700 turns of No. 26 AWG enamel
 covered magnet wire closely spaced. The coil is finished with
 six coats of polyurethane sealer to reduce corona loss.

 The primary coil is an Archimedes spiral (flat "pancake" coil)
 consisting of 9 turns of 3/8-inch wide, .02-inch thick beryllium
 copper strip tapped at about 7 turns. The turn to turn spacing
 is 3/8-inch. Spacing between the first turn of the primary and
 the secondary is 3/4-inch. A single open turn of copper is
 spaced around the outer turn of the primary to protect the
 primary from direct strikes. This open turn is grounded.

 The spark gaps consists of four fixed gaps in series. These gaps
 were constructed using tungsten tipped electrodes which can be
 purchased new from arc welder supply companies.

 The capacitor is four .003 microfarad, 30 KV Hi-K Ceramic, RF
 rated Sprague "hockey pucks" in parallel. The measured value is
 .012 microfarads capacitance with is supplied by two 9000 volt
 60 mA neon sign transformers in parallel (only one transformer
 was connected when this photo was taken). The input voltage is
 controlled by a 22 ampere, 0-140 volt Powerstat.

 This coil was built and operated by Gary Legel, 1306 Sheppard
 Drive, Fullerton, CA  92631  USA